FUNCTIONAL TEST – Process CHW System

University of Michigan Plant Extension

Commissioning and Plan Review Department

Phone (734) 615-7168 Fax (734) 936-3334

This is not a punch list.  The engineer of record, not the commissioning team, performs Punch listing.

Project Name: XXX					Project Number: XXXX-XX-XXX

Tag No.			Model No.			Serial No.

Attendees:

1) _________________________________________ 2)____________________________________

3) _________________________________________ 4)____________________________________

5) _________________________________________ 6)____________________________________

7) _________________________________________ 8)____________________________________

Is system operating or is this initial start-up? __________________________________________________

Is the Pre-Start Checklist Complete? ________________________________________________________

Is all piping complete? ___________________________________________________________________

Pump CHWP-5

Pump mfg. start-up report obtained: _______________________________________________________

Pump data plate legible: ________________________________________________________________

Pump rotation verified: _________________________________________________________________

Flexible connections not torqued/mis-aligned: ________________________________________________

Flexible connection restraining bolts not over tighten: __________________________________________

Inertia base clears floor and is free to move? __________________________________________________

Dead head pump, run at full speed, record pressure differential: ___________________________________

Pump dead head pressure matches curve dead head?: ___________________________________________

System at maximum flow, pump at full speed, record motor current:

Motor Amp Draw: L1__________ L2 ____________ L3______________

Rated Motor Amps: ___________ each phase

Are the amp reading at each phase similar?__________________________________________________

Are the amp reading at or below the rated motor amps? ________________________________________

Unusual vibration? ______________________________________________________________________

Unusual noise? _________________________________________________________________________

Pump CHWP-6

Pump mfg. start-up report obtained: _______________________________________________________

Pump data plate legible: ________________________________________________________________

Pump rotation verified: _________________________________________________________________

Flexible connections not torqued/mis-aligned: ________________________________________________

Flexible connection restraining bolts not over tighten: __________________________________________

Inertia base clears floor and is free to move? __________________________________________________

Dead head pump, run at full speed, record pressure differential: ___________________________________

Pump dead head pressure matches curve dead head?: ___________________________________________

System at maximum flow, pump at full speed, record motor current:

Motor Amp Draw: L1__________ L2 ____________ L3______________

Rated Motor Amps: ___________ each phase

Are the amp reading at each phase similar?__________________________________________________

Are the amp reading at or below the rated motor amps? ________________________________________

Unusual vibration? ______________________________________________________________________

Unusual noise? _________________________________________________________________________

VSD for CHWP-5

VSD mfg. start-up report obtained __________________________________________________________

VSD H-O-A tested ______________________________________________________________________

VSD bypass switch test __________________________________________________________________

VSD Start-Stop by DDC _________________________________________________________________

VSD Status to DDC _____________________________________________________________________

VSD input signal (AO) test _______________________________________________________________

VSD output (AI)________________________________________________________________________

Early break contacts verified______________________________________________________________

No vibration through-out speed range _______________________________________________________

UM plant approves drive installation ________________________________________________________

VSD for CHWP-6

VSD mfg. start-up report obtained __________________________________________________________

VSD H-O-A tested ______________________________________________________________________

VSD bypass switch test __________________________________________________________________

VSD Start-Stop by DDC _________________________________________________________________

VSD Status to DDC _____________________________________________________________________

VSD input signal (AO) test _______________________________________________________________

VSD output (AI)________________________________________________________________________

Early break contacts verified______________________________________________________________

No vibration through-out speed range _______________________________________________________

UM plant approves drive installation ________________________________________________________

Flow meters

Pump CHWP-5 flow meter installed in correct flow direction? ___________________________________

Pump CHWP-6 flow meter installed in correct flow direction? ___________________________________

Correct upstream and downstream straight pipe for pump flow meters? ____________________________

Loop by-pass meter install in correct flow direction? ___________________________________________

Loop by-pass meter is powered up? _________________________________________________________

Minimum of 10 pipe diameters upstream and downstream of loop flow meter? ______________________

General

Vents at high points? ____________________________________________________________________

Drains at low points? ____________________________________________________________________

Pump vents installed per detail? ___________________________________________________________

Gages positioned to be readable____________________________________________________________

Gage scale ranges reasonable______________________________________________________________

Dirt/grime cleaned up____________________________________________________________________

Remarks:

## Completed by (print): _______________________Company: __________________________

Signed: _______________________________________ Date: _________________________________