Commissioning Sequence Progress Check Sheet

System: LSI Chilled Water Systems

Overview: A 20 inch chilled water supply and return line comes from the tunnel into the second level mechanical room.  The system then splits into three pumped tertiary loops, one for the Lab and Office Chilled Water System, one for the Vivarium Chilled Water System, and one for the Process Chilled Water System.

The Vivarium Chilled Water System uses pumps CHWP-3 and 4 and serves AHU-3, 4, 5, and 6 on the second level.

The Process Chilled Water System uses pumps CHWP-5 and 6 and serves AHU-1, 2, 7, and 8 on the second level.

The Lab and Office Chilled Water System uses pumps CHWP-1 and 2 and serves AHU-9, 10, 11, and 12 in the penthouse; AHU-13 at the first floor; fan coil units on level 2; environmental room condensing units on levels 3, 4, 5, and 6; lab equipment EQ-20 on level 3; and AHU-15 on level 3.

Commissioning Sequence Progress Check Sheet

System: Vivarium Chilled Water Systems

Cx Sequence:

Initial acknowledgment and date when item is complete.

Acknowledgements

Owner		Contractor

Shop Drawings Approved

_____			Valves

_____ 			Pumps CHWP-3, 4

_____		Major Components Delivered

_____		Pre-Installation Checklist Completed (Pumps)

_____          _____       	Installation Instructions Provided

_____		_____ 		Pipe / Pump alignment confirmed

UM Cx to view before bolting pipe to pump flanges.

_____		Installations Complete

_____		Controls Complete (subcontractor)

_____		Controls Complete (UM DDC)

_____		Pressure Testing Complete

_____         _____     	Flushing/Cleaning Plan Submitted/Approved

_____		_____		Flushing Complete

_____		_____		Pre-start Check Sheet Complete

_____	     	 _____		Start – up Notification Submitted

_____		_____		Functional Testing Check Sheet Complete

_____         _____      	Training Scheduled

_____         _____      	Training Completed

_____      	All Punch-list Items Completed

_____ 		_____		Contract Commissioning Requirements Completed

Commissioning Sequence Progress Check Sheet

System: Process Chilled Water Systems

Cx Sequence:

Initial acknowledgment and date when item is complete.

Acknowledgements

Owner		Contractor

Shop Drawings Approved

_____			Valves

_____ 			Pumps CHWP-5, 6

_____		Major Components Delivered

_____		Pre-Installation Checklist Completed (Pumps)

_____          _____       	Installation Instructions Provided

_____		_____ 		Pipe / Pump alignment confirmed

UM Cx to view before bolting pipe to pump flanges.

_____		Installations Complete

_____		Controls Complete (subcontractor)

_____		Controls Complete (UM DDC)

_____		Pressure Testing Complete

_____         _____     	Flushing/Cleaning Plan Submitted/Approved

_____		_____		Flushing Complete

_____		_____		Pre-start Check Sheet Complete

_____	     	 _____		Start – up Notification Submitted

_____		_____		Functional Testing Check Sheet Complete

_____         _____      	Training Scheduled

_____         _____      	Training Completed

_____      	All Punch-list Items Completed

_____ 		_____		Contract Commissioning Requirements Completed

Commissioning Sequence Progress Check Sheet

System: Lab and Office Chilled Water Systems

Cx Sequence:

Initial acknowledgment and date when item is complete.

Acknowledgements

Owner		Contractor

Shop Drawings Approved

_____			Valves

_____ 			Pumps CHWP-1, 2

_____		Major Components Delivered

_____		Pre-Installation Checklist Completed (Pumps)

_____          _____       	Installation Instructions Provided

_____		_____ 		Pipe / Pump alignment confirmed

UM Cx to view before bolting pipe to pump flanges.

_____		Installations Complete

_____		Controls Complete (subcontractor)

_____		Controls Complete (UM DDC)

_____		Pressure Testing Complete

_____         _____     	Flushing/Cleaning Plan Submitted/Approved

_____		_____		Flushing Complete

_____		_____		Pre-start Check Sheet Complete

_____	     	 _____		Start – up Notification Submitted

_____		_____		Functional Testing Check Sheet Complete

_____         _____      	Training Scheduled

_____         _____      	Training Completed

_____      	All Punch-list Items Completed

_____ 		_____		Contract Commissioning Requirements Completed