Pre-Start Check List

University of Michigan

Facilities Evaluation and Commissioning Dept.

Phone (734) 615-7168  Fax (734) 936-3334

This document shall be filled out by the contractor and provided to the UM Commissioning Engineer in advance of actual equipment start-up.  Note "NA" for not applicable, "NO" for problem or non-compliance .  This document is to be used in conjunction with the manufacturer's pre-start check list.

Project Name:

Project Number:

Completed by/representing (print):

# Fans

Tag No. 			Model No. 				Serial No.

Check		Item					Comments

General

Inertia base vibration isolators (aligned, weight even distributed, free floating)

Preliminary alignment complete (belts)

Preliminary belt tension checked and corrected

Fan and motor correctly supported

Grouted

No grout shrinkage indicating wrong grout or concrete used

Grout extends under channel base

Channel base supported on wedges

Fan off/rotate by hand/no drag

Fan data label secure, legible and undamaged.

Fan data label info matches approved submittal

Flex Duct connections correctly installed

Flexible connection not torqued/mis-aligned

5 Dia. straight inlet duct diameters

Gages positioned to be readable

Gage scale ranges reasonable

Duct Hangers-

Correct type

Correct installation

Vapor barrier integrity (no tears, punctures, gaps, lagging lapped onto insul shields, etc.)

Spring Isolator Hangers-

Correct type

Correct location

Spring on bottom, rubber on top

Housing can fully rotate without contacting adjacent obstructions

No sort circuits

Certification:  I certify the above checks have been made (signed/date)