PRE-START CHECKLIST- 3.39 Lab Exhaust – Strobic Fans

University of Michigan Plant Extension

Commissioning & Plan Review Department

Phone (734) 615-7168 Fax (734) 936-3334

This document shall be filled out by the contractor and provided to the UM Commissioning Engineer at least 7 days in advance of the actual equipment start-up. Note “NA” for not applicable or “NO” for problem or non-compliance. This document is to be used in conjunction with the manufacturer’s pre-start checklist.

Project Name: XXX					Project Number: XXXX-XX-XXX

Tag No. 			Model No. 				Serial No.

##### LEF-4a

LEF-4b

LEF-4c

LEF-4d

Check		Item					Comments

General

Plenum/stand clamps tight

Actuators accessible and mounted out of main air stream 						 No visible damage to fans, plenums or coatings

Isolation dampers adjusted and epoxy coated

Disconnect installed

Fan off/rotate by hand/no drag

Fan data label secure, legible and undamaged.

Fan data label info matches approved submittal

By-pass dampers adjusted

Bird Screen installed on by-pass damper acoustical louver

Motor HP correct

Fan speed correct

Are all flanges sealed with caulk

Fan/ plenum connection sealed with neoprene pad and no air  leaks

Grease leads filled and bearings greased								 Bump motor, check fan rotation

Check for air leaks at plenum and fan

Check for reverse “wind-milling” on each fan

Duct -

Correct type

Supported from roof correctly									 Duct weather protected

Duct sealed at wall penetration

Duct insulated properly

Correct supports

Controls-

Controls pre-start list complete

Controls Complete (UM DDC)

Controls Complete (Subcontractor)

Isolation dampers open/close

By-pass dampers modulate

By-pass dampers closed when system is off

Fans stage on/off

Fan System Functional Test:

___ Functional Test scheduled for: ____________________, to be conducted by: ____________________

___ Functional Test notification provided to commissioner 7 days in advance of scheduled test.

Remarks:

## Completed by (print): _______________________Company: __________________________

Signed: _______________________________________ Date: _________________________________