Commissioning Sequence Progress Check Sheet

System: Misc. Exhaust System

EF-13

EF-13

West Toilet Exhaust Fan

Location: Penthouse Roof

Airflow: 4,400 cfm

Overview: The fan removes air from the toilet rooms at each floor on the west side of the building.

Controls: 	Dwg M9-1.11, Control Type P.

The exhaust fan runs continuously and has a current sensor for input to the DDC.

Supply boxes maintain a constant airflow to each toilet room.

A room thermostat modulates a reheat coil at each box to maintain room temperature.

Cx Sequence:

Initial acknowledgment and date when item is complete.

Acknowledgments

Owner		Contractor

_____		Shop Drawings Approved: Fans, Supply Boxes, Controls

_____	Major Components Delivered  Fans, Boxes

_____		Pre-Installation Check Sheets Complete (Fan)

_____		    _____		Installation Manuals Submitted (Fan)

_____		Mechanical Complete

_____		Electrical Complete

_____		Controls Complete (subcontractor)

_____		Controls Complete (UM DDC)

_____		Pre-start-up check sheet complete

_____		    _____		Balancing Complete

_____	     	    _____		Start – up Notification Submitted

_____		    _____		Functional Test Check Sheet completed

_____		All Punch-list Items Completed

_____		    _____		Training Scheduled

_____		    _____		Training Complete

_____		    _____		Contract Commissioning Requirements Completed

Commissioning Sequence Progress Check Sheet

System: Misc. Exhaust System

EF-14

EF-14

East Toilet Exhaust Fan

Location: Penthouse Roof

Airflow: 3,800 cfm

Overview: The fan removes air from the toilet rooms at each floor on the east side of the building.

Controls: 	Dwg M9-1.11, Control Type P.

The exhaust fan runs continuously and has a current sensor for input to the DDC.

Supply boxes maintain a constant airflow to each toilet room.

A room thermostat modulates a reheat coil at each box to maintain room temperature.

Cx Sequence:

Initial acknowledgment and date when item is complete.

Acknowledgments

Owner		Contractor

_____		Shop Drawings Approved: Fans, Supply Boxes, Controls

_____	Major Components Delivered  Fans, Boxes

_____		Pre-Installation Check Sheets Complete (Fan)

_____		    _____		Installation Manuals Submitted (Fan)

_____		Mechanical Complete

_____		Electrical Complete

_____		Controls Complete (subcontractor)

_____		Controls Complete (UM DDC)

_____		Pre-start-up check sheet complete

_____		    _____		Balancing Complete

_____	     	    _____		Start – up Notification Submitted

_____		    _____		Functional Test Check Sheet completed

_____		All Punch-list Items Completed

_____		    _____		Training Scheduled

_____		    _____		Training Complete

_____		    _____		Contract Commissioning Requirements Completed

Commissioning Sequence Progress Check Sheet

System: Misc. Exhaust System

EF-15

EF-15

Hazardous Storage Exhaust Fan

Location: Second Floor Roof

Airflow: 550 cfm

Overview: The fan removes air from second floor storage rooms 2453A and 2453B.

Controls: 	Dwg M9-1.11, Control Type Y.

The exhaust fan runs continuously and has a current sensor for input to the DDC.

A Phoenix supply box maintains a constant airflow to each room.

A room thermostat modulates a reheat coil at the box to maintain room temperature.

Cx Sequence:

Initial acknowledgment and date when item is complete.

Acknowledgments

Owner		Contractor

_____		Shop Drawings Approved: Fans, Supply Boxes, Controls

_____	Major Components Delivered  Fans, Boxes

_____		Pre-Installation Check Sheets Complete (Fan)

_____		    _____		Installation Manuals Submitted (Fan)

_____		Mechanical Complete

_____		Electrical Complete

_____		Controls Complete (subcontractor)

_____		Controls Complete (UM DDC)

_____		Pre-start-up check sheet complete

_____		    _____		Balancing Complete

_____	     	    _____		Start – up Notification Submitted

_____		    _____		Functional Test Check Sheet completed

_____		All Punch-list Items Completed

_____		    _____		Training Scheduled

_____		    _____		Training Complete

_____		    _____		Contract Commissioning Requirements Completed

Commissioning Sequence Progress Check Sheet

System: Misc. Exhaust System

EF-16

EF-16

Hazardous Storage Exhaust Fan

Location: Second Floor Roof

Airflow: 850 cfm

Overview: The fan removes air from second floor storage rooms 2452 and 2458.

Controls: 	Dwg M9-1.11, Control Type Y.

The exhaust fan runs continuously and has a current sensor for input to the DDC.

Two Phoenix supply boxes maintain a constant airflow to each room.

A room thermostat modulates a reheat coil at each box to maintain room temperature.

Cx Sequence:

Initial acknowledgment and date when item is complete.

Acknowledgments

Owner		Contractor

_____		Shop Drawings Approved: Fans, Supply Boxes, Controls

_____	Major Components Delivered  Fans, Boxes

_____		Pre-Installation Check Sheets Complete (Fan)

_____		    _____		Installation Manuals Submitted (Fan)

_____		Mechanical Complete

_____		Electrical Complete

_____		Controls Complete (subcontractor)

_____		Controls Complete (UM DDC)

_____		Pre-start-up check sheet complete

_____		    _____		Balancing Complete

_____	     	    _____		Start – up Notification Submitted

_____		    _____		Functional Test Check Sheet completed

_____		All Punch-list Items Completed

_____		    _____		Training Scheduled

_____		    _____		Training Complete

_____		    _____		Contract Commissioning Requirements Completed

Commissioning Sequence Progress Check Sheet

System: Misc. Exhaust System

## EF-17

EF-17

Hazardous Storage Exhaust Fan

Location: Second Floor Roof

Airflow: 125 cfm

Overview: The fan removes air from second floor storage room 2465.

Controls: 	Dwg M9-1.11, Control Type Y.

The exhaust fan runs continuously and has a current sensor for input to the DDC.

A duct tap from an adjacent Phoenix supply box system maintains a constant airflow to this room.

A thermostat in an adjacent room modulates a reheat coil at the box to maintain room temperature.

Cx Sequence:

Initial acknowledgment and date when item is complete.

Acknowledgments

Owner		Contractor

_____		Shop Drawings Approved: Fans, Supply Boxes, Controls

_____	Major Components Delivered  Fans, Boxes

_____		Pre-Installation Check Sheets Complete (Fan)

_____		    _____		Installation Manuals Submitted (Fan)

_____		Mechanical Complete

_____		Electrical Complete

_____		Controls Complete (subcontractor)

_____		Controls Complete (UM DDC)

_____		Pre-start-up check sheet complete

_____		    _____		Balancing Complete

_____	     	    _____		Start – up Notification Submitted

_____		    _____		Functional Test Check Sheet completed

_____		All Punch-list Items Completed

_____		    _____		Training Scheduled

_____		    _____		Training Complete

_____		    _____		Contract Commissioning Requirements Completed

Commissioning Sequence Progress Check Sheet

System: Misc. Exhaust System

EF-18

EF-18

Hazardous Storage Exhaust Fan

Location: Second Floor Roof

Airflow: 850 cfm

Overview: The fan removes air from second floor storage rooms 2453D, 2453E, 2453F and 2457.

Controls: 	Dwg M9-1.11, Control Type Y.

The exhaust fan runs continuously and has a current sensor for input to the DDC.

Two Phoenix supply boxes maintain a constant airflow to each room.

Two room thermostats modulate reheat coils at each box to maintain room temperature.

Cx Sequence:

Initial acknowledgment and date when item is complete.

Acknowledgments

Owner		Contractor

_____		Shop Drawings Approved: Fans, Supply Boxes, Controls

_____	Major Components Delivered  Fans, Boxes

_____		Pre-Installation Check Sheets Complete (Fan)

_____		    _____		Installation Manuals Submitted (Fan)

_____		Mechanical Complete

_____		Electrical Complete

_____		Controls Complete (subcontractor)

_____		Controls Complete (UM DDC)

_____		Pre-start-up check sheet complete

_____		    _____		Balancing Complete

_____	     	    _____		Start – up Notification Submitted

_____		    _____		Functional Test Check Sheet completed

_____		All Punch-list Items Completed

_____		    _____		Training Scheduled

_____		    _____		Training Complete

_____		    _____		Contract Commissioning Requirements Completed